## Slide 1: Data Representation in Memory CSCI 2400 / ECE 3217: Computer Architecture
Instructor:
David Ferry
Slides adapted from Bryant & O’Hallaron’s slides via Jason Fritts

## Slide 2: Data Representation in Memory
Basic memory organization
Bits & Bytes – basic units of Storage in computers
Representing information in binary and hexadecimal
Representing Integers
  Unsigned integers
  Signed integers
Representing Text
Representing Pointers

## Slide 3: Byte-Oriented Memory Organization
Modern processors: Byte-Addressable Memory
  Conceptually a very large array of bytes
  Each byte has a unique address
  Processor address space determines address range:
    32-bit address space has 232 unique addresses: 4GB max
      0x00000000 to 0xffffffff (in decimal: 0 to 4,294,967,295)
    64-bit address space has 264 unique addresses: ~ 1.8x1019 bytes max
      0x0000000000000000 to 0xffffffffffffffff
      Enough to give everyone on Earth about 2 Gb
  Address space size is not the same as processor size!
    E.g.: The original Nintendo was an 8-bit processor with a 16-bit address space
• • •
0x00•••0
0xFF•••F

## Slide 4: Data Representation in Memory
Basic memory organization
Bits & Bytes – basic units of Storage in computers
Representing information in binary and hexadecimal
Representing Integers
  Unsigned integers
  Signed integers
Representing Text
Representing Pointers

## Slide 5: Why Use Bits & Binary?
0.0V
0.5V
2.8V
3.3V
0
1
0
Digital transistors operate in high and low voltage ranges
Voltage Range dictates Binary Value on wire
  high voltage range (e.g. 2.8V to 3.3V) is a logic 1
  low voltage range (e.g. 0.0V to 0.5V) is a logic 0
  voltages in between are indefinite values
Ternary or quaternary systems have practicality problems

## Slide 6: Bits & Bytes
Computers use bits:
  a “bit” is a base-2 digit
  {L, H} => {0, 1}
Single bit offers limited range, so grouped in bytes
  1 byte = 8 bits
  a single datum may use multiple bytes
Data representation 101:
  Given N bits, can represent 2N unique values
    Letters of the alphabet?
    Colors?

## Slide 7: Encoding Byte Values
Processors generally use multiples of Bytes
  common sizes: 1, 2, 4, 8, or 16 bytes
  Intel data names:
    Byte 1 byte (8 bits) 28 = 256
    Word 2 bytes (16 bits) 216 = 65,536
    Double word 4 bytes (32 bits) 232 = 4,294,967,295
    Quad word 8 bytes (64 bits) 264 = 18,446,744,073,709,551,616
Unfortunately, these names are not standard
so we’ll often use C data names instead
(but these vary in size too… /sigh)

## Slide 8: C Data Types
C Data Type | Typical 32-bit | Intel IA32 | x86-64
char | 1 byte | 1 | 1
short | 2 | 2 | 2
int | 4 | 4 | 4
long | 4 | 4 | 8
long long | 8 | 8 | 8
float | 4 | 4 | 4
double | 8 | 8 | 8
long double | 8 | 10/12 | 10/16
pointer (addr) | 4 | 4 | 8
32-bit
64-bit
key
differences

## Slide 9: Data Representation in Memory
Basic memory organization
Bits & Bytes – basic units of Storage in computers
Representing information in binary and hexadecimal
Representing Integers
  Unsigned integers
  Signed integers
Representing Text
Representing Pointers

## Slide 10: Encoding Byte Values
1 Byte = 8 bits
  Binary: 000000002 to 111111112
A byte value can be interpreted in many ways!
  depends upon how it’s used
For example, consider byte with: 010101012
  as ASCII text: ‘U’
  as integer: 8510
  as IA32 instruction: pushl %ebp
  the 86th byte of memory in a computer
  a medium gray pixel in a gray-scale image
  could be interpreted MANY other ways…

## Slide 11: Binary is Hard to Represent!
Problem with binary – Cumbersome to use
  e.g. approx. how big is: 10100111010100010111010112 ?
  Would be nice if the representation was closer to decimal: 21,930,731
Let’s define a larger base so that
  for equivalence, R and x must be integers – then 1 digit in R equals x bits
  equivalence allows direct conversion between representations
  two options closest to decimal:
    octal: (base eight)
    hexadecimal: (base sixteen)

## Slide 12: Representing Binary Efficiently
Octal or Hexadecimal?
  binary : 10100111010100010111010112
  octal: 1235213538
  hexadecimal number: 14EA2EB16
  decimal: 21930731
Octal and Hex are closer in size to decimal, BUT…
How many base-R digits per byte?
  Octal: 8/3 = 2.67 octal digits per byte -- BAD
  Hex: 8/4 = 2 hex digits per byte -- GOOD
Hexadecimal wins: 1 hex digit  4 bits

## Slide 13: Expressing Byte Values
Common ways of expressing a byte
  Binary: 000000002 to 111111112
  Decimal: 010 to 25510
  Hexadecimal: 0016 to FF16
    Base-16 number representation
    Use characters ‘0’ to ‘9’ and ‘A’ to ‘F’
    in C/C++ programming languages, D316 written as either
      0xD3
      0xd3
Juliet: "What's in a name? That which we call a rose By any other name would smell as sweet."

## Slide 14: Decimal vs Binary vs Hexadecimal
Decimal | Binary | Hexadecimal
0 | 0000 | 0
1 | 0001 | 1
2 | 0010 | 2
3 | 0011 | 3
4 | 0100 | 4
5 | 0101 | 5
6 | 0110 | 6
7 | 0111 | 7
8 | 1000 | 8
9 | 1001 | 9
10 | 1010 | A
11 | 1011 | B
12 | 1100 | C
13 | 1101 | D
14 | 1110 | E
15 | 1111 | F
16 | 10000 | 10
17 | 10001 | 11
18 | 10010 | 12

## Slide 15: Convert Between Binary and Hex
Convert Hexadecimal to Binary
  Simply replace each hex digit with its equivalent 4-bit binary sequence
  Example: 6 D 1 9 F 3 C16
Convert Binary to Hexadecimal
  Starting from the radix point, replace each sequence of 4 bits with the equivalent hexadecimal digit
  Example: 1011001000110101110101100010100112
0110 1101 0001 1001 1111 0011 11002
1 6 4 6 B A C 5 316

## Slide 16: Data Representation in Memory
Basic memory organization
Bits & Bytes – basic units of Storage in computers
Representing information in binary and hexadecimal
Representing Integers
  Unsigned integers
  Signed integers
Representing Text
Representing Pointers

## Slide 17: Unsigned Integers – Binary
Computers store Unsigned Integer numbers in Binary (base-2)
  Binary numbers use place valuation notation, just like decimal
  Decimal value of n-bit unsigned binary number:
0 | 1 | 1 | 1 | 0 | 1 | 0 | 1
27
26
25
24
23
22
21
20

## Slide 18: Unsigned Integers – Base-R
Convert Base-R to Decimal
  Place value notation can similarly determine decimal value of any base, R
  Decimal value of n-digit base r number:
  Example:

## Slide 19: Unsigned Integers – Hexadecimal
Commonly used for converting hexadecimal numbers
  Hexadecimal number is an “equivalent” representation to binary, so often need to determine decimal value of a hex number
  Decimal value for n-digit hexadecimal (base 16) number:
  Example:

## Slide 20: Unsigned Integers – Convert Decimal to Base-R
Also need to convert decimal numbers to desired base
Algorithm for converting unsigned Decimal to Base-R
  Assign decimal number to NUM
  Divide NUM by R
    Save remainder REM as next least significant digit
    Assign quotient Q as new NUM
  Repeat step b) until quotient Q is zero
Example:
NUM
R
REM
Q
least significant digit
most significant digit

## Slide 21: Unsigned Integers – Convert Decimal to Binary
Example with Unsigned Binary:
NUM
R
REM
Q
least significant digit
most significant digit

## Slide 22: Unsigned Integers – Convert Decimal to Hexadecimal
Example with Unsigned Hexadecimal:
NUM
R
REM
Q
least significant digit
most significant digit

## Slide 23: Unsigned Integers – Ranges
Range of Unsigned binary numbers based on number of bits
  Given representation with n bits, min value is always sequence
    0....0000 = 0
  Given representation with n bits, max value is always sequence
    1....1111 = 2n – 1
  So, ranges are:
    unsigned char:
    unsigned short:
    unsigned int:
1 | 1 |    | 1 | 1 | 1 | 1
2n-1
2n-2
23
22
21
20

## Slide 24: Data Representation in Memory
Basic memory organization
Bits & Bytes – basic units of Storage in computers
Representing information in binary and hexadecimal
Representing Integers
  Unsigned integers
  Signed integers
Representing Text
Representing Pointers

## Slide 25: Signed Integers – Binary
Signed Binary Integers converts half of range as negative
Signed representation identical, except for most significant bit
  For signed binary, most significant bit indicates sign
    0 for nonnegative
    1 for negative
  Must know number of bits for signed representation
-27
26
25
24
23
22
21
20
Signed Integer representation:
27
26
25
24
23
22
21
20
Unsigned Integer representation:
Place value of
most significant bit
is negative
for signed binary

## Slide 26: Signed Integers – Binary
Decimal value of n-bit signed binary number:
Positive (in-range) numbers have same representation:
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
-27
26
25
24
23
22
21
20
Signed Integer representation:
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
27
26
25
24
23
22
21
20
Unsigned Integer representation:

## Slide 27: Signed Integers – Binary
Only when most significant bit set does value change
Difference between unsigned and signed integer values is 2N
0 1 | 1 | 1 | 0 | 1 | 0 | 0 | 1
-27
26
25
24
23
22
21
20
Signed Integer representation:
0 1 | 1 | 1 | 0 | 1 | 0 | 0 | 1
27
26
25
24
23
22
21
20
Unsigned Integer representation:

## Slide 28: Quick Check:
For an 8-bit representation:
What bit pattern has the minimum value?
What bit pattern has the maximum value?
What bit pattern represents 0?
What bit pattern represents -1?

## Slide 29: Signed Integers – Ranges
Range of Signed binary numbers:
  Given representation with n bits, min value is always sequence
    100....0000 = – 2n-1
  Given representation with n bits, max value is always sequence
    011....1111 = 2n-1 – 1
  So, ranges are:
C data type | # bits | Unsigned range | Signed range
char | 8 | 0  255 | -128  127
short | 16 | 0  65,535 | -32,768  32,767
int | 32 | 0  4,294,967,295 | -2,147,483,648  2,147,483,647

## Slide 30: Signed Integers – Convert to/from Decimal
Convert Signed Binary Integer to Decimal
  Easy – just use place value notation
    two examples given on last two slides
Convert Decimal to Signed Binary Integer
  MUST know number of bits in signed representation
  Algorithm:
    Convert magnitude (abs val) of decimal number to unsigned binary
    Decimal number originally negative?
      If positive, conversion is done
      If negative, perform negation on answer from part a)
        zero extend answer from a) to N bits (size of signed repr)
        negate: flip bits and add 1

## Slide 31: Signed Integers – Convert Decimal to Base-R
Example:
  A)
NUM
R
REM
Q
least significant bit
most significant bit

## Slide 32: Signed Integers – Convert Decimal to Base-R
Example:
  B) -3710 was negative, so perform negation
    zero extend 100101 to 8 bits
    negation
      flip bits:
      add 1:
Can validate answer using
place value notation

## Slide 33: Quick check:
For an 8-bit representation:
Convert 6710 into a signed integer

## Slide 34: Signed Integers – Convert Decimal to Base-R
Example:
  A)
NUM
R
REM
Q
least significant bit
most significant bit

## Slide 35: Signed Integers – Convert Decimal to Base-R
Example:
  B) 6710 was positive, so done
Can validate answer using
place value notation

## Slide 36: Quick check:
For an 8-bit representation:
Convert -10010 into a signed integer

## Slide 37: Signed Integers – Convert Decimal to Base-R
Example:
  A)
NUM
R
REM
Q
least significant bit
most significant bit

## Slide 38: Signed Integers – Convert Decimal to Base-R
Example:
  B) -10010 was negative, so perform negation
    zero extend 100101 to 8 bits
    negation
      flip bits:
      add 1:
Can validate answer using
place value notation

## Slide 39: Signed Integers – Convert Decimal to Base-R
Be careful of range!
Example:
  A)
  B) -18310 was negative, so perform negation
    zero extend 10110111 to 8 bits // already done
    negation
      flip bits:
      add 1:
not -18310… WRONG!
-18310 is not in valid range
for 8-bit signed

## Slide 40: Representation of Signed Integers
Multiple possible ways:
  Sign magnitude
  Ones’ Complement
  Two’s Complement (what has been presented)
Two’s Complement greatly simplifies addition & subtraction in hardware
  We’ll see why when we cover operations
  Generally the only method still used

## Slide 41: Representation of Signed Integers
Why the name Two’s Complement?
  For a w-bit signed representation, we represent -x as 2w – x
  E.g.: consider the 8-bit representation of
(unsigned)
(signed)

## Slide 42: Data Representation in Memory
Basic memory organization
Bits & Bytes – basic units of Storage in computers
Representing information in binary and hexadecimal
Representing Integers
  Unsigned integers
  Signed integers
Representing Text
Representing Pointers

## Slide 43: Representing Strings
char S[6] = "18243";
Strings in C
  Represented by array of characters
  Each character encoded in ASCII format
    Standard 7-bit encoding of character set
    Character “0” has code 0x30
  String should be null-terminated
    Final character = 0
  ASCII characters organized such that:
    Numeric characters sequentially increase from 0x30
      Digit i has code 0x30+i
    Alphabetic characters sequentially increase in order
      Uppercase chars ‘A’ to ‘Z’ are 0x41 to 0x5A
      Lowercase chars ‘A’ to ‘Z’ are 0x61 to 0x7A
    Control characters, like <RET>, <TAB>, <BKSPC>, are 0x00 to 0x1A
Intel / Linux
0x31
0x38
0x32
0x34
0x33
0x00
‘1’
‘8’
‘2’
‘4’
‘3’
null term

## Slide 44: Representing Strings
Limitations of ASCII
  7-bit encoding limits set of characters to 27 = 128
  8-bit extended ASCII exists, but still only 28 = 256 chars
  Unable to represent most other languages in ASCII
Answer: Unicode
  first 128 characters are ASCII
    i.e. 2-byte Unicode for ‘4’: 0x34 -> 0x0034
    i.e. 4-byte Unicode for ‘T’: 0x54 -> 0x00000054
  UTF-8: 1-byte version // commonly used
  UTF-16: 2-byte version // commonly used
    allows 216 = 65,536 unique chars
  UTF-32: 4-byte version
    allows 232 = ~4 billion unique characters
  Unicode used in many more recent languages, like Java and Python
UTF-16 on Intel
0x31
0x00
0x38
0x00
0x32
0x00
0x34
0x00
0x33
0x00
0x00
0x00
‘1’
‘8’
‘2’
‘4’
‘3’
null term

## Slide 45: String Representation Links
ASCII
  http://www.ascii-code.com/
Unicode
  http://unicode-table.com/en/

## Slide 46: Quick Check:
Convert the following strings to ASCII-
char school[4] = “SLU”;
char name[6] = “Frank”;

## Slide 47: Data Representation in Memory
Basic memory organization
Bits & Bytes – basic units of Storage in computers
Representing information in binary and hexadecimal
Representing Integers
  Unsigned integers
  Signed integers
Representing Text
Representing Pointers

## Slide 48: What is a Pointer?
Recall:
Memory is a contiguous array of individual bytes
  Consider a machine with 16-bit addresses
0x0000
0x0001
0x0002
0x0003
0x0004

## Slide 49: What is a Pointer?
Recall:
Memory is a contiguous array of individual bytes
  Consider a machine with 16-bit addresses
unsigned X = 15398; //0x00003C26
26
3C
00
00
0x0000
0x0001
0x0002
0x0003
0x0004

## Slide 50: What is a Pointer?
Points to a location in memory
Suppose:
unsigned X = 15398; //0x00003C26
unsigned *ptr = &X; //0xA244
A pointer is a variable that holds the address of another variable
Different compilers and machines assign different locations to objects
26
3C
00
00
0x44
0xA2
0xA244
0xA245
0xA246
0xA247

## Slide 51: Quick Check
Consider the string: char S[6] = “HELLO”;
What is S[0] ?
What is &S[0] ?
What is S[3]?
What is &S[3]?
0x48
0x45
0x4C
0x4C
0x4F
0x00
‘H’
‘E’
‘L’
‘L’
‘O’
null term
0xACED
0xACEE
0xACEF
0xACF0
0xACF1
0xACF2