## Slide 1: Linux Boot Process on the Raspberry Pi 2
David Ferry, Chris Gill
CSE 522S - Advanced Operating Systems
Washington University in St. Louis
St. Louis, MO 63143

## Slide 2: Raspberry Pi 2 Hardware
Broadcom BCM2836 system-on-a-chip (SoC)
  VideoCore IV GPU
  Cortex-A7 CPU
  1GB RAM
At power on:
  GPU enabled
  CPU disabled
  RAM disabled
  Filesystem disabled

## Slide 3: Bootstrap Process
The boot loader enables hardware:
At power on:
  GPU loads and executes proprietary first stage from ROM
First stage:
  GPU loads and executes /boot/bootcode.bin on SD card
  Loads into L2 Cache
Second stage (bootcode.bin):
  GPU loads and executes /boot/start.elf
  Enables and loads into RAM
Third stage (start.elf):
  GPU loads kernel7.img into RAM
  Reads configuration files
  Activates CPU 0

## Slide 4: GPU Boot Loaders
The GPU Loaders (bootcode.bin and start.elf) are proprietary:
Source code is unavailable
Compilers are unavailable
Low-level actions:
  Enables low-level SD card access
  Enables memory
  Sets up kernel arguments and loads kernel image
  Configures and enables CPU 0 to start executing kernel

## Slide 5: System State After GPU Boot Loaders
Physical memory map:
Kernel arguments (ATAGS) usually loaded at 0x100
Available RAM
Where the kernel is located in physical memory
Misc. low level info (display, terminal, etc.)
Kernel command line arguments
To start kernel:
CPU in supervisor mode
Interrupts disabled
MMU and address translation must be off
Data cache must be off
Register r1 holds machine type
Register r2 holds address of kernel arguments
Jump to starting address of kernel (usually 0x8000)
Kernel usually loaded at 0x8000
Low 32KB
Extra Space

## Slide 6: Kernel Entry Point
What happens after the boot loader jumps to 0x8000?
At compile time, the kernel was arranged so that instructions at 0x8000 will start the kernel
/arch/arm/kernel/head.S is _the_ entry point
Actions:
  Queries processor features
  Manually builds initial page tables
  Sets up and turns on memory management unit

## Slide 7: Kernel Entry Point - Continued
Control moves to /arch/arm/kernel/head-common.S
Function __mmap_switched():
  Saves important pointers in registers
  Manages transition from physical to virtual memory
  Jumps to start_kernel()

## Slide 8: Transition to start_kernel()
At this point:
  RAM is enabled
  CPU 0 is enabled and executing kernel
  Page table has been constructed
  Memory management unit is active
But:
  No kernel execution stack
  No other services

## Slide 9: start_kernel()
Function start_kernel() in /init/main.c:
  Initializes kernel lock protectors
  Sets up stack protectors at top and bottom of kernel stack memory region
  Sets up timing and scheduling kernel subsystems before enabling interrupts
  Enables interrupts
  Sets up other subsystems
  Creates init and kthreadd threads
  Starts other CPUs in system
  Goes into CPU idle/scheduler loop